## Slide 1: Point System Overview
An early slot is an asset (more valuable than a late slot) – buy/sell earlier slot
If I want to take off early, I buy an earlier slot (#slots earlier = # points)
  The seller earns points from buyer
  Trade request to sell (earlier) slot must be made in Extended Virtual Queue (>schedule pushback time)
If I want to take off later, I sell my earlier slot
  The buyer spends points to get earlier slot. Buyer must be willing & “able”.
  Able is = time available > time request

## Slide 2: Point System Overview
Airline departure slots “missed” are assessed penalty if ADFMS not notified early enough
  Notification needs to occur is prior to scheduled push-back time
  Penalties suspended until threshold exceeded
ADFMS allows ‘falling back’ to later departure slot due to an unforeseen circumstances
  Bump up/ compression by subsequent flights in queue to ensure queue efficiency
Points awarded periodically / unused points expire periodically
Point exchange first-in first out (FIFO)
Unfilled departure slots can be acquired without exchanging points
No buying when points < 0

## Slide 3: Points Based on Periodic Reset
Notes:
Point total = Number of points added per period + Number of points added by sales within the time period – Number of points subtracted with buys within the time period.
The example above is based on 40 points for 4 weeks.
Airline XX

## Slide 4: Rolling Points Based on Weeks
Airline XX
Expiring Points
10 points acquired each week

## Slide 5: Point systems
 | Rolling Points | Periodic Reset
Trading patterns | Generally consistent trading patterns over time. | Trading will likely vary based on current time within reset period.
Unlimited points | Loss of points outside of point total window removes the possibility of unlimited point totals | Reset period removes the possibility of unlimited point totals
Notes:
Don’t want too many points thereby making everyone a buyer
Don’t want too few points to where buying can’t be initiated
Companies gathering large amounts of points needs to be avoided in order to maintain interest in the program.

## Slide 6: Points Per Company
Notes:
System needs to appear fair
Companies can trade between their own flights without affecting their point totals.
Equal distribution
  Companies with a lot of points per flight (e.g. 9e) tend to become buyers as they will have surplus points
  Companies with lower points per flight (e.g. US) may tend to trade within their own schedule at least for buys
Varying points by airport use
  Companies with lower points (e.g. 9E – 6 points) have a difficult time initiating trading until they can sell some slots.
  Companies with a lot of points (e.g. US – 188 points) tend to become buyers and can also trade within their own schedule.

## Slide 7: Trade For An Earlier Departure
Original Departure Slot (Blue)
8:00am
9:00am
Available for Trade Slot (Red)
12 minutes (8 slots)
Scheduled Departures
Expected Departures
Trade Window
Notes:
Each slot is 1 minute & 30 seconds.
The processing of the change needs to occur prior to the recalculated expected departure time. This may or may not be the same as the current expected departure time because of the difference in location of the aircraft making the switch.
Processing Time
Recalculated departure (Blue)

## Slide 8: Trade For A Later Departure
Original Departure Slot (Blue)
8:00am
9:00am
Available for Trade Slot (Red)
12 minutes (8 slots)
Scheduled Departures
Expected Departures
Trade Window
Notes:
Each slot is 1 minute & 30 seconds.
The processing of the change needs to occur prior to the recalculated expected departure time. This may or may not be the same as the current expected departure time because of the difference in location of the aircraft making the switch.
Processing Time
Recalculated departure (Blue)

## Slide 9: Later Departure Slot Excursions
Trade available (See previous slide)
No trade available, open slot achieved through departure slot shifting
No trade available, open slot available due to lack of traffic
No trade available, no open slot available
Slot that needs to go later
Slots shifting
Unaffected slots